## Slide 1: High Throughput Compression of Double-Precision Floating-Point Data
Martin Burtscher and Paruj Ratanaworabhan
School of Electrical and Computer Engineering
Cornell University

## Slide 2: Introduction
Scientific programs
  Produce and transfer lots of 64-bit FP data
    Exchange 100s of MB/s, generate 1TB/day of new data
Large amounts of data
  Are expensive to store and transfer
  Take a long time to transfer
Data compression
  Can reduce amount of data
  Can speed up transfer

## Slide 3: IEEE 754 Double-Precision Values
Goal
  Compress linear streams of FP data fast and well
  Online operation and lossless compression
Challenges
  Floating-point data are hard to compress
    FP codes may generate over 90% unique values
Related work on lossless FP compression
  Focuses on 32-bit single-precision values
  Relies on smoothness of data or known geometry

## Slide 4: Floating-Point Data Compression
Our approach
  Predict FP data with value prediction algorithms and encode the difference
  Format:
Value predictors
  Hardware devices to speed up processors
  Predict instruction result by extrapolating previously sequences of computed results
  Employ very fast and simple algorithms

## Slide 5: FPC Algorithm
Make two predictions
Select closer value
XOR with true value
Count leading zeros
Encode value
Update predictors

## Slide 6: Algorithm/Implementation Co-Design
Inner loop (about 50 and 70 C statements)
  Compresses or decompresses one block of data
  Accounts for over 90% of execution time
Loop body optimizations
  Loop body is used to hide memory latency
  No fp, int mult, or int div instructions
  No branches (only conditional moves)
  Single basic block (>100 machine instructions)
  Average IPC > 5.4 and 5.1 on Itanium 2

## Slide 7: Evaluation Method
System
  1.6 GHz Itanium 2, Intel C Itanium Compiler 9.1
  Red Hat Enterprise Linux AS4
Scientific datasets
  Linear streams of 64-bit FP data (18 – 277MB)
  4 observations: spitzer, temp, error, info
  4 simulations: comet, plasma, brain, control
  5 messages: bt, lu, sp, sppm, sweep3d

## Slide 8: Compression Throughput

## Slide 9: Decompression Throughput

## Slide 10: Summary and Conclusions
FPC algorithm
  Highest throughput and mean compression ratio
  1.02 – 15.05 absolute compression ratio
  840 and 680 MB/s throughput on a 1.6GHz Itanium 2 (= 2 and 2.5 machine cycles per byte)
  http://www.csl.cornell.edu/~burtscher/research/FPC/
Conclusions
  Value predictors are fast & accurate data models
  Algorithm/implementation co-design is essential