## Slide 1: On the Compressibility of Floating-Point Data in Posit and IEEE-754 Representation
Andrew Rodriguez* and Martin Burtscher
Department of Computer Science

## Slide 2: Floating-Point Arithmetic
IEEE-754: primary real number representation
  Used extensively in scientific computing
Floating-point operations have problems
  Finite precision and accuracy
  Inconsistent results based on implementation
Less precise types (float16, float8, etc.)
  Can speed up computation at the cost of accuracy

## Slide 3: Posit Representation
Introduced as a direct drop-in replacement
  Alleviates some issues with the IEEE-754 standard
Variable-length fraction and exponent
  Larger dynamic range
  Higher accuracy than IEEE floats of the same size
Many prior comparisons of posits to floats
  Convert float data to posit data in experiments
  Hardware units have been tested in simulators
  Posits are more accurate and in some cases faster

## Slide 4: Scientific Applications
Applications emit huge amounts of float data
  HACC generates petabytes of data in one simulation
Certain applications need higher accuracy
  Use posits instead of floats
  However, no prior work on compressibility of posits
HACC Visualization (ornl.gov)

## Slide 5: This Work
Studies compressibility of posits and floats
  Takes existing float data and converts to posit data
  Compares the compression ratios of both encodings
Investigates 5 existing lossless compressors
  Along with several newly synthesized compressors
Uses 14 single-precision inputs from SDRBench
  From 7 different scientific domains

## Slide 6
Float and Posit
Representations
6

## Slide 7: IEEE-754 Floats
A float has 3 fields: sign, exponent and mantissa
A 32-bit float has
  Sign bit, 8-bit biased exponent, 23-bit mantissa
Can represent normal values and special values
  Subnormals, Not-a-Number (NaNs), +/- infinity

## Slide 8: Posits
A posit has 4 fields
  Sign, regime, exponent and fraction
  The regime acts as additional scaling of the exponent
All fields but the sign have variable-length
Posits are most accurate for values close to 1.0

## Slide 9: Posit<n, es>
A posit is parameterized by n and es
  n is the total number of bits
  es is the maximum number of exponent bits
  Together create a posit<n, es> number

## Slide 10: Posit<32, es> Regime
Regime r is computed by counting identical bits
  k identical bits terminated by an opposite bit
  If regime starts with a 0, r = -k
  If regime starts with a 1, r = k - 1

## Slide 11: Posit<32, es> Exponent & Fraction
The exponent begins after the regime
  Is stored as an unsigned integer with no bias
The rest of the bits make up the fraction
  There is an implicit 1 bit just like with IEEE floats
Negative posits are encoded in 2’s complement

## Slide 12: Posit<32, es> Special Values
There are only 2 special values
  Zero: all bits are 0
  Not-a-Real (NaR): sign bit is set, followed by all 0s
Posits have no subnormals

## Slide 13: Numeric Value of a Posit
Compute fraction f with the following formula
  m is the number of fraction bits
  F is the fraction bitstring
The posit value v is computed with

## Slide 14
Experimental
Methodology
14

## Slide 15: Datasets
7 SDRBench datasets from different domains

## Slide 16: Inputs
14 single-precision inputs, 2 from each dataset

## Slide 17: Float to Posit
Use the cppposit library for conversion
For each float input, copy and encode as posit
Use 32-bit posits with es=3 for our experiments
Standard 32-bit posit use es=2
  We found that es=3 preserves more floats losslessly
  es=3 yields 97.1% precise values
  es=2 yields 85.6% precise values

## Slide 18: LC Framework
LC generates compression algorithms
  Can be lossless and lossy
  Based on a library of data transformations
LC chains transformations together
  Yields many possible compression algorithms
  Generated 512,000 3-stage pipelines (80 components)

## Slide 19: Compressors
5 lossless general-purpose compressors
  bzip2, gzip, lz4, XZ, Zstd
Generate several new compressors with LC
  1 compressor for all float inputs
  1 compressor for all posit inputs
Customized compressor approach
  1 LC compressor per input, 28 in total
We report the geometric-mean compression ratio

## Slide 20
Results

## Slide 21: Float Compression Ratios
Highest: XZ
  Best dictionary approach
  Followed by LC
Lowest: lz4
  lz4 designed for speed
Zstd, bzip2, gzip
  Roughly the same CR

## Slide 22: Posit Compression Ratios
Highest: XZ
  Again, followed by LC
Lowest: lz4
Lower than float data
  1.85-3.62% reduction in CR
  bzip2 compresses better
  lz4 remains the same

## Slide 23: Histogram of Float Exponent Values
Most expo. around 128
  Most values close to 1.0
QRAIN, CLOUD, ICEFRAC
  Contain many zeros and subnormal values
Posits are more accurate for values close to 1.0
QRAIN compresses better in posit format
  Due to loss in accuracy

## Slide 24: Customized Pipeline CR
Floats compress better
  But not by much
Custom LC pipelines
  On par with XZ

## Slide 25: Conclusion
First study on posit compressibility
XZ provides highest compression on both formats
Customized LC pipelines on par with XZ
  But faster and CPU/GPU compatible
Posit compressibility slightly lower than floats
  Storing scientific data in posit format is a viable option
Converting float to posit may incur some loss
  Aim to natively use posits to avoid this loss

## Slide 26: Future Work
Study other metrics
  Compression/decompression throughput
  Memory overhead
  Other values for es
Create special-purpose posit compressors
  Compare against special-purpose float compressors

## Slide 27: Thank you!
Acknowledgments
  Department of Energy, reviewers
Contact information
  andrew.rodriguez@txstate.edu